## Slide 1
LeNet CNN 加速器内部模块与数据流图
Internal Datapath and Control Flow of Vitis HLS LeNet Accelerator
CNN Accelerator IP (Vitis HLS Generated) HLS top: lenet_full_top
AXI4 Master
Data Ports
feature_in
weight
bias = 0
feature_out
Controller
ap_ctrl_hs
start / done / idle / ready
Input Buffer
Weight Buffer
Feature Buffer
Output Buffer
Computing Module
Window Generator
5×5 Sliding Window
PE Array / MAC Engine
Multiply-Accumulate
Accumulator + ReLU
MaxPool Processor
2×2, stride=2
Dense / FC Processor
LeNet Layer Schedule
Conv1 → ReLU → Pool1
Conv2 → ReLU → Pool2
Conv3 → ReLU
FC1 → ReLU
FC2 → Logits
Classification Result
Digit 0–9
Solid blue line: data path | Dashed orange line: control path | Data layout: CHW feature maps / OIHW conv weights / [out][in] FC weights